## Slide 1: Chapter 6 Information Sources and Signals
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
1
Notes: 1

## Slide 2
PPTs are from lecture slides of
Computer Networks and Internets, 6th Ed. by Douglas E. Comer, Pearson

## Slide 3: What Is Data Communications?
Broad field of study
Usually associated with the Physical Layer
Touches on
  – Physics
  – Mathematics
  – Engineering
Includes
  Transmission of signals
  Encoding data
  Modulation and multiplexing

## Slide 4: 6.3 Analog and Digital Signals
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
4
Data communications deals with two types of information:
  analog
  digital
An analog signal is characterized by a continuous mathematical function
A digital signal has a fixed set of valid levels
Figure 6.1 illustrates the concept
  by showing examples of how the signals from an analog source and a digital source vary over time
Notes: 4

## Slide 5
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
5
6.3 Analog and Digital Signals
Notes: 5

## Slide 6
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
6
6.5 Sine Waves and Signal Characteristics
Notes: 6

## Slide 7: 6.5 Sine Waves and Signal Characteristics
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
7
Important characteristics of signals that relate to sine waves:
Frequency:
  the number of oscillations per unit time (usually seconds)
Amplitude:
  the difference between the maximum and minimum signal heights
Phase:
  how far the start of the sine wave is shifted from a reference time
Wavelength:
  the length of a cycle as a signal propagates across a medium
  is determined by the speed with which a signal propagates
These characteristics can be expressed mathematically
  Figure 6.3 illustrates the frequency, amplitude, and phase characteristics
Notes: 7

## Slide 8
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
8
6.5 Sine Waves and Signal Characteristics
Notes: 8

## Slide 9: 6.5 Sine Waves and Signal Characteristics
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
9
The frequency can be calculated as the inverse of the time required for one cycle, which is known as the period
The example sine wave in Figure 6.3a has
  a period T = 1 seconds
  and a frequency of 1 / T or 1 Hertz
The example in Figure 6.3b has
  a period of T = 0.5 seconds
  its frequency is 2 Hertz
Both examples are considered extremely low frequencies
Typical communication systems use high frequencies
To clarify high frequencies, engineers express time in fractions of a second or express frequency in units such as megahertz (MHz)
Figure 6.4 lists time scales and common prefixes used with frequency
Notes: 9

## Slide 10
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
10
6.5 Sine Waves and Signal Characteristics
Notes: 10

## Slide 11
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
11
6.6 Composite Signals
Notes: 11

## Slide 12
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
12
6.8 Time and Frequency Domain Representations
Notes: 12

## Slide 13: 6.9 Bandwidth of an Analog Signal
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
13
What is network bandwidth?
In networking and communication, the definition of bandwidth varies; here we describe analog bandwidth
  We define the bandwidth of an analog signal to be the difference between the highest and lowest frequencies of the constituent parts (the highest and the lowest frequencies obtained by Fourier analysis)
Figure 6.7 shows a frequency domain plot with frequencies measured in Kilohertz (KHz)
  Such frequencies are in the range audible to a human ear
  In the figure, the bandwidth is the difference between the highest and lowest frequency (5 KHz - 1 KHz = 4 KHz)
Notes: 13

## Slide 14
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
14
6.9 Bandwidth of an Analog Signal
Notes: 14

## Slide 15
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
15
6.10 Digital Signals and Signal Levels
Notes: 15

## Slide 16: 6.11 Baud and Bits Per Second
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
16
As with signal levels, the hardware in a practical system places limits on how short the time can be
  if the signal does not remain at a given level long enough, the receiving hardware will fail to detect it
The accepted measure of a communication system does not specify a length of time
  how many times the signal can change per second, which is defined as the baud
  for example, if a system requires the signal to remain at a given level for .001 seconds, we say that the system operates at 1000 baud
Both baud and number of signal levels control bit rate
Notes: 16

## Slide 17: 6.11 Baud and Bits Per Second
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
17
If a system with two signal levels operates at 1000 baud
  the system can transfer exactly 1000 bits per second
If a system that operates at 1000 baud has four signal levels
  the system can transfer 2000 bits per second (because four signal levels can represent two bits)
Equation 6.1 expresses the relationship between baud, signal levels, and bit rate
Notes: 17

## Slide 18: 6.13 The Bandwidth of a Digital Signal
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
18
What is the bandwidth of a digital signal?
If Fourier analysis is applied to a square wave?
A digital signal has infinite bandwidth
  because Fourier analysis of a digital signal produces an infinite set of sine waves with frequencies that grow to infinity
Notes: 18

## Slide 19: 6.16 Manchester Encoding Used in Computer Networks
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
19
One particular standard for line coding is especially important for networks:
  Manchester Encoding used with Ethernet
Detecting a transition in signal level is easier than measuring the signal level
This fact explains why Manchester Encoding uses transitions rather than levels to define bits
In Manchester Encoding, a 1 corresponds to a transition from negative voltage level to a positive voltage level
  Correspondingly, a 0 corresponds to a transition from a positive voltage level to a negative level
  The transitions occur in the “middle” of the time slot of a bit
Figure 6.13a illustrates the concept
Notes: 19

## Slide 20
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
20
6.16 Manchester Encoding Used in Computer Networks
Notes: 20

## Slide 21: 6.17 Converting an Analog Signal to Digital
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
21
Many sources of information are analog
  which means they must be converted to digital form for further processing (e.g., before they can be encrypted)
In PCM, the level of an analog signal is measured repeatedly at fixed time intervals and converted to digital form
The acronym PCM is ambiguous
  because it can refer to the general idea or to a specific form of pulse code modulation used by the telephone system
Figure 6.14 illustrates the steps
Notes: 21

## Slide 22
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
22
6.17 Converting an Analog Signal to Digital
Notes: 22

## Slide 23
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
23
6.17 Converting an Analog Signal to Digital
Notes: 23

## Slide 24: 6.18 The Nyquist Theorem and Sampling Rate
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
24
An analog signal must be sampled in PCM or DM
How frequently should an analog signal be sampled?
  Taking too few samples (undersampling) means that the digital values only give a crude approximation of the original signal
  Taking too many samples (oversampling) means that more digital data will be generated, which uses extra bandwidth
A mathematician named Nyquist discovered the answer to the question of how much sampling is required:
  where fmax is the highest frequency in the composite signal
Nyquist Theorem provides a practical solution to the problem:
  sample a signal at least twice as fast as the highest frequency that must be preserved
Notes: 24

## Slide 25: 6.19 Nyquist Theorem and Telephone System Transmission
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
25
Consider the telephone system that was originally designed to transfer voice as an example
  Measurements of human speech have shown that preserving frequencies between 0 - 4000 Hz provides acceptable audio quality
When converting a voice signal from analog to digital
  the signal should be sampled at a rate of 8000 samples per second
The PCM standard used by the phone system quantifies each sample into an 8 bit value for quality
  the range of input is divided into 256 possible levels so that each sample has a value between 0 and 255
The rate generated for a single telephone call is:
Notes: 25

## Slide 26: Chapter 7 Transmission Media
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
26
Notes: 26

## Slide 27
PPTs are from lecture slides of
Computer Networks and Internets, 6th Ed. by Douglas E. Comer, Pearson

## Slide 28: 7.1 Introduction
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
28
This chapter
  continues the discussion of data communications
  considers transmission media, including wired, wireless, and optical media
  gives a taxonomy of media types
  introduces basic concepts of electromagnetic propagation
  explains how shielding can reduce or prevent interference and noise
  explains the concept of capacity
Notes: 28

## Slide 29: 7.3 A Taxonomy by Forms of Energy
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
29
Notes: 29

## Slide 30: 7.5 Twisted Pair Copper Wiring
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
30
The third fact in the previous section explains the wiring used with communication systems
There are three forms of wiring that help reduce interference from electrical noise
  Unshielded Twisted Pair (UTP)
    also known as twisted pair wiring
  Coaxial Cable
  Shielded Twisted Pair (STP)
Twisting two wires makes them less susceptible to electrical noise than leaving them parallel as shown in Figure 7.2
Notes: 30

## Slide 31: 7.5 Twisted Pair Copper Wiring
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
31
Notes: 31

## Slide 32: 7.6 Shielding: Coaxial Cable and Shielded Twisted Pair
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
32
Forms of wiring are available that have extra metal shielding
The most familiar form is the wiring used for cable television
  known as coaxial cable (coax)
  the wiring has a thick metal shield formed from braided wires that completely surround a center (inner) wire that carries the signal
Figure 7.3 illustrates the concept
  The shield in a coaxial cable forms a flexible cylinder around the inner wire
  The barrier also prevents signals on the inner wire from radiating electromagnetic energy
A coaxial cable can be placed adjacent to sources of electrical noise and other cables, and can be used for high frequencies
Notes: 32

## Slide 33: 7.6 Shielding: Coaxial Cable and Shielded Twisted Pair
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
33
Notes: 33

## Slide 34: 7.6 Shielding: Coaxial Cable and Shielded Twisted Pair
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
34
Using braided wire instead of a solid metal shield keeps coaxial cable flexible
variation is known as shielded twisted pair (STP)
  The cable has a thinner, more flexible metal shield surrounding one or more twisted pairs of wires
  In most versions of STP cable, the shield consists of metal foil, similar to the aluminum foil used in a kitchen
Notes: 34

## Slide 35: 7.7 Categories of Twisted Pair Cable
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
35
Notes: 35

## Slide 36: Media Using Light Energy
InfraRED transmission (short range and low data rate)
Point-to-point lasers (useful between buildings)
Optical fiber (high data rate and long distance)

## Slide 37: 7.8 Media Using Light Energy and Optical Fibers
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
37
The most important and widely used type is optical fiber
Each fiber consists of a thin strand of glass or transparent plastic encased in a plastic cover
  An optical fiber is used for communication in a single direction
  One end of the fiber connects to a laser or LED used to transmit light
  The other end of the fiber connects to a photosensitive device used to detect incoming light
To provide two-way communication
  two fibers are used; one to carry information in each direction
Transmission: LED or Injection Laser Diode (ILD)
Reception: photo-sensitive cell or photodiode
  LEDs and photo-sensitive cells are used for short distances and slower bit rates common with multimode fiber;
Notes: 37

## Slide 38: 7.10 Optical Fiber Compared to Copper Wiring
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
38
Notes: 38

## Slide 39: 7.11 Infrared (IR) Communication Technologies
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
39
IR uses the same type of energy as a TV remote control:
  a form of electromagnetic radiation that behaves like visible light but falls outside the range that is visible to a human eye
Like visible light, infrared disperses quickly
Infrared signals can reflect from a smooth, hard surface
IR commonly used to connect to a nearby peripheral
The wireless aspect of infrared can be attractive for laptop computers
Notes: 39

## Slide 40: 7.12 Point-to-Point Laser Communication
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
40
A pair of devices with a beam that follows the line-of-sight
IR is classified as providing point-to-point communication
Other point-to-point communication technologies also exist
  One form of point-to-point communication uses a beam of coherent light produced by a laser
Laser communication follows line-of-sight, and requires a clear, unobstructed path between the communicating sites
Notes: 40

## Slide 41: 7.13 Electromagnetic (Radio) Communication
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
41
Notes: 41

## Slide 42: 7.16 GEO Communication Satellites
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
42
Notes: 42

## Slide 43: 7.16 GEO Communication Satellites
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
43
The distance required for a geostationary orbit is 35,785 kilometers or 22,236 miles
  which is approximately one tenth the distance to the moon
What does such a distance mean for communication?
  consider a radio wave traveling to a GEO satellite and back
  at the speed of light, 310 meters per second, the trip takes:
A delay of approximately 0.2 seconds can be significant for some applications
  For electronic transactions such as a stock exchange offering a limited set of bonds, delaying an offer by 0.2 seconds may mean the difference between a successful and unsuccessful offer
Notes: 43

## Slide 44: 7.19 Tradeoffs Among Media Types
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
44
The choice of medium is complex
Choice involves the evaluation of multiple factors, such as:
  Cost
    materials, installation, operation, and maintenance
  Data rate
    number of bits per second that can be sent
  Delay
    time required for signal propagation or processing
  Affect on signal
    attenuation and distortion
  Environment
    susceptibility to interference and electrical noise
  Security
    susceptibility to eavesdropping
Notes: 44

## Slide 45: 7.20 Measuring Transmission Media
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
45
The two most important measures of performance used to assess a transmission medium:
  Propagation delay
    the time required for a signal to traverse the medium
  Channel capacity
    the maximum data rate that the medium can support
Nyquist discovered a fundamental relationship between the bandwidth of a transmission system and its capacity to transfer data known as Nyquist Theorem
  It provides a theoretical bound on the maximum rate at which data can be sent without considering the effect of noise
  If a transmission system uses K possible signal levels and has a hardware bandwidth B, the maximum data rate in bits per second, D, is
Notes: 45

## Slide 46: 7.21 The Effect of Noise on Communication
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
46
Nyquist's Theorem provides an absolute maximum that cannot be achieved in practice
  Nyquist’s Theorem gives us hope: using more signal levels can increase the data rate
  a real system is subject to small amounts of electrical noise
Claude Shannon extended Nyquist's work to specify the maximum data rate that could be achieved over a transmission system that experiences noise (electrical noise in the universe limits the effective channel capacity of any practical communication system
  The result, called Shannon's Theorem
    C is the effective limit on the channel capacity in bits per second
    B is the hardware bandwidth
    S/N is the signal-to-noise ratio
Notes: 46

## Slide 47: Assignment
<Assignment>
Show the rate at which two digital voice data are sent using the PCM in the same digital telephone system?
2. Find information on “wireshark”, and install in on your computer. What is the latest version of “wireshark”.
Send your results to me by email.
This assignment will be used to check attendance.