## Slide 1: 컴퓨터 네트워크 Computer Networks and Internets, 6e

## Slide 2: Review
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
2
Information (Signal) to Signal
  Analog to Analog
  ; Modulation (Demodulation) - MODEM
  Analog to Digital
  ; PCM
  Digital to Analog
  ; Shift Keying (Modulation)
  Digital to Digital
  ; Line (Coding) - CODEC
Notes: 2

## Slide 3: Chapter 11 Multiplexing and Demultiplexing (Channelization)

## Slide 4: 11.1 Introduction
This chapter
  continues the discussion of data communications by introducing multiplexing
  describes the motivation
  defines basic types of multiplexing that are used throughout computer networks and the Internet
  explains how modulated carriers provide the basis for many multiplexing mechanisms

## Slide 5
11.2 The Concept of Multiplexing

## Slide 6: 11.3 The Basic Types of Multiplexing
There are four basic approaches to multiplexing that each have a set of variations and implementations
  Frequency Division Multiplexing (FDM)
  Wavelength Division Multiplexing (WDM)
  Time Division Multiplexing (TDM)
  Code Division Multiplexing (CDM)
TDM and FDM are widely used
WDM is a form of FDM used for optical fiber
CDM is a mathematical approach used in cell phone mechanisms

## Slide 7
11.4 Frequency Division Multiplexing

## Slide 8
11.4 Frequency Division Multiplexing

## Slide 9
11.4 Frequency Division Multiplexing

## Slide 10: 11.7 Wavelength Division Multiplexing
Form of FDM used with light (i.e., on an optical fiber)
Separate frequencies called colors or lambdas
Prisms used to separate frequencies
Current technology is Dense WDM (DWDM); an individual
channel can provide 10 Gbps

## Slide 11: 11.8 Time Division Multiplexing (TDM)
  multiplexing in time simply means transmitting an item from one source, then transmitting an item from another source, and so on

## Slide 12: 11.9 Synchronous TDM

## Slide 13: 11.10 Framing Used in the Telephone System Version of TDM

## Slide 14: Hierarchical TDM (data rates of Leased Circuits: T-standard)
basic rate T1(24) T2(96) T3(672)

## Slide 15: 11.12 The Problem with Synchronous TDM: Unfilled Slots

## Slide 16: 11.13 Statistical TDM

## Slide 17: 11.15 Code Division Multiplexing (CDM)
CDM used in parts of the cellular telephone system and for some satellite communication
  The specific version of CDM used in cell phones is known as Code Division Multi-Access (CDMA)
CDM relies on an interesting mathematical idea
Each sender is assigned a unique binary code Ci
  that is known as a chip sequence
  Senders multiply the data value by their chip sequence
  Transmitted value is a sum of all senders
  Each receiver multiplies incoming value by its chip sequence to extract data
Advantage over statistical TDM: lower delay when network loaded

## Slide 18: Chapter 12 Access and Interconnection Technologies
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
18
Notes: 18

## Slide 19: Review
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
19
Multiplxesing
  TDM
  Synchronous, Statistical
  FDM
  CDM
Solving Assignment
Notes: 19

## Slide 20: 12.1 Introduction
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
20
This chapter
  concludes the discussion of data communications by examining two facilities used in the Internet
  discusses access technologies, such as dialup, DSL, and cable modems
  considers high-capacity digital circuits used in the core of the Internet
  expands the discussion of the telephone system multiplexing hierarchy
  focuses on the data communications aspects of the technologies by considering multiplexing and data rates
Notes: 20

## Slide 21: 12.2 Internet Access Technology: Upstream and Downstream
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
21
Internet access technology refers to a data communications system that connects an Internet subscriber to an ISP
  such as a telephone company or cable company
Most Internet users follow an asymmetric pattern
  a subscriber receives more data from the Internet than sending
    a browser sends a URL that comprises a few bytes
    in response, a web server sends content
Downstream to refer to data traveling from an ISP in the Internet to a subscriber
Upstream to refer to data traveling from a subscriber to an ISP
Notes: 21

## Slide 22: 12.2 Internet Access Technology: Upstream and Downstream
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
22
Notes: 22

## Slide 23: 12.3 Narrowband and Broadband Access Technologies
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
23
A variety of technologies are used for Internet access
They can be divided into two broad categories based on the data rate they provide
  Narrowband (less than 128Kbps) ; Dialup, ISDN, is disappearing
  Broadband (more than 1Mbps) ; DSL, Cable Modems, Wireless
In networking terms, network bandwidth refers to data rate
Notes: 23

## Slide 24: 12.5 Digital Subscriber Line (DSL) Technologies
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
24
DSL is one of the main technologies used to provide high-speed data communication services over a local loop
Figure 12.4 (below) lists DSL variants
  Because the names differ only in the first word, the set is collectively referred to by the acronym xDSL
Notes: 24

## Slide 25: 12.5 Digital Subscriber Line (DSL) Technologies
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
25
ADSL is the most widely deployed variant
  and the one that most residential customers use
ADSL uses FDM to divide the bandwidth of the local loop into three regions
  one of the regions corresponds to traditional analog phone service, which is known as Plain Old Telephone Service (POTS)
  two regions provide data communication: 255 downstream,31 up
Figure 12.5 (below) illustrates how ADSL divides bandwidth
Notes: 25

## Slide 26: 12.9 Cable Modem Technologies
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
26
A variety of wireless and wired technologies have been developed for use in the local loop
Send data over Community Antenna TeleVision (CATV) coaxial cable system
Standard is DOCSIS (Data-Over-Cable Service Interface Specification)
Ver. 1.x uses FDM to deliver TV signals over coaxial cable
Coaxial cable has high bandwidth and is less susceptible to electromagnetic interference than twisted pair
Max. downstream rate is 52Mbps
Bandwidth shared among multiple subscribers
Each subscriber receives 1/N of the bandwidth
Notes: 26

## Slide 27: 12.13 Access Technologies That Employ Optical Fiber
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
27
HFC(Hybrid Fiber Coax) can provide high-speed data communications
  a HFC system uses a combination of optical fibers and coaxial cables
Other access technologies
Notes: 27

## Slide 28: Other Access Technologies
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
28
Network (Ethernet)
Wireless
  – Wi-Fi
  – WIMAX
  – Satellite
  3G and 4G cellular services
Leased point-to-point circuits (e.g., T1 or fractional T1)
Notes: 28

## Slide 29: A closer look at network structure:
network edge:
  hosts: clients and servers
  servers often in data centers
access networks, physical media: wired, wireless communication links
network core:
  interconnected routers
  network of networks
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 30: 12.20 Highest Capacity Data Circuits
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
30
STS standards specify copper interface
OC standards specify optical fiber interface
Suffix C on OC-standards means single channel
Notes: 30

## Slide 31: Assignment
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
31
1. We need to use synchronous TDM and combine 10 digital sources, each of 800bps. Each output slot carries 8 bits from each source, but one extra bit(framing bit) is added to each frame.
a) what is the size of an output frame in bits?
b) What is the output data rate(bps)?
2. Compare the throughput of the following transmissions.
a) parallel vs. serial b) FDM vs. TDM
c) full-duplex vs. half-duplex d) synchronous vs. asynchronous
3. Explain the multiplexing method used in ADSL.
Send your solution to me by email. (Due date: 4.11. )
This assignment will be used to check your attendance.
Notes: 31