## Slide 1: 컴퓨터 네트워크 Computer Networks and Internets, 6e

## Slide 2: PART III Packet Switching and Network Technologies An overview of packet switching and packet technologies that use wired and wireless media
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
2
Notes: 2

## Slide 3: Solving Problems
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
3
1. A synchronous TDM combining 10 digital sources, each of 800bps. Each output slot carries 8 bits from each source, but one extra bit(framing bit) is added to each frame.
2. Compare the throughput of the following transmissions.
a) parallel vs. serial b) FDM vs. TDM
c) full-duplex vs. half-duplex d) synchronous vs. asynchronous
3. Explain the multiplexing method used in ADSL.
Notes: 3

## Slide 4: Chapter 13 Local Area Networks: Packets, Frames, and Topologies
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
4
Notes: 4

## Slide 5: 13.1 Introduction
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
5
This chapter
  begins the part of the text that examines packet switching and computer network technologies
  explains the IEEE standards model
  concentrates on the concepts of hardware addressing and frame identification
Later chapters
  expand the discussion by considering the use of packets in Wide Area Networks
  cover a variety of wired and wireless networking technologies that accept and deliver packets
Notes: 5

## Slide 6: Networks
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
6
Distinct from physical communication systems
Attach multiple endpoints
Two broad categories
  Circuit switched
  Packet switched
Notes: 6

## Slide 7: Circuit Switched Networks
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
7
Provide point-to-point communication between pairs of endpoints
Establish path between sender and receiver
Separate steps for circuit creation, use, and termination
Performance equivalent to an isolated physical path
Circuit can be
  Permanent/ provisioned (left in place for long periods)
  Switched (created on demand)
Concept: user leases piece of underlying infrastructure for a time period
Notes: 7

## Slide 8: Packet Switched Networks
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
8
Form the basis for the Internet
Multiplex communication over shared media
All data divided into packets (maximum size fixed)
After sending one packet, sender allows others a chance to transmit before sending a second packet
Arbitrary, asynchronous communication
No set-up required before communication begins
Performance varies due to statistical multiplexing
Concept: underlying infrastructure is shared among users
Notes: 8

## Slide 9: 13.2 Circuit Switching
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
9
Circuit switching provides 1-to-1 dedicated connections
Notes: 9

## Slide 10: 13.3 Packet Switching
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
10
Packet switching provides statistical TDM sharing
Notes: 10

## Slide 11: Categories Of Packet Switched Networks
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
11
Packet switching technologies are commonly classified according to the distance they span
  LAN, MAN, WAN
  PAN, SAN(storage), CAN(chip)
Below summarizes the terminology used
Notes: 11

## Slide 12: 13.5 Standards for Packet Format and Identification
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
12
Notes: 12

## Slide 13: 13.6 IEEE 802 Model and Standards
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
13
IEEE Project 802 (LAN/MAN standards committee)
  divides Layer 2 of the protocol stack into two conceptual sub-layers,
  The Logical Link Control (LLC)
    sublayer specifies addressing and the use of addresses for demultiplexing as described later in the chapter
  The Media Access Control (MAC)
    sublayer specifies how multiple computers share underlying medium
Notes: 13

## Slide 14
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
14
Figure 13.6
Examples of the identifiers IEEE has assigned to various LAN
standards
Notes: 14

## Slide 15: Standards Define
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
15
Network topology (shape)
Endpoint addressing scheme
Frame (packet) format
Media access mechanism
Physical layer aspects and wiring
Notes: 15

## Slide 16: 13.8 LAN Topologies
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
16
Notes: 16

## Slide 17: 13.8 LAN Topologies 13.8.5 The Reason for Multiple Topologies
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
17
Each topology has advantages and disadvantages
A ring makes it easy for computers to coordinate access and to detect whether the network is operating correctly
  However, an entire ring network is disabled if one of the cables is cut
A star helps protect the network from damage to a single cable because each cable connects only one machine
A bus requires fewer wires than a star, but has the same disadvantage as a ring
  a network is disabled if someone accidentally cuts the main cable
Later chapters that describe specific network technologies provide additional details about differences
Notes: 17

## Slide 18: Assignment
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
18
Name the two sublayers of Layer 2 protocol defined by IEEE, and give the purpose of each.
What are the characteristics of LANs and WANs?
Send your solution to me by email. (Due date: 4.18. )
This assignment will be used to check your attendance.
Notes: 18

## Slide 19: IEEE Standard For Addressing
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
19
IEEE Media Access Control address(MAC address)
  Informally called an Ethernet address
  Assigned to Network Interface Card (NIC)
  there is a 3-byte Organizationally Unique ID (OUI)
    OUI identifies the equipment vendor
    a 3-byte block that identifies a particular NIC
Notes: 19

## Slide 20: Review (Solving Problems)
Show the rate at which two digital voice data are sent using the PCM in the same digital telephone system?
2. How CRC and checksum are produced in the real protocol?
Why is CRC located at the tail of the packet?
Why is Checksum located at the header of the packet?
3. What can a RAC scheme achieve that a single parity bit scheme cannot?

## Slide 21: Review
The fundamental abstraction used to collect protocols into a unified whole is known as a ( )
All aspects of a communication problem can be partitioned into pieces that work together
  each piece is known as a ( )
Internet protocols use a ( )-layer reference model
How can a pair of applications that run on two independent computers coordinate to guarantee that they request a connection at the same time?
=>The answer lies in a form of interaction known as the ( )
  A ( ) starts first and awaits contact
  A ( ) starts second and initiates the connection
4. Explain the multiplexing method used in ADSL.

## Slide 22
Headers and Layers

## Slide 23: Review
How many times the signal can change per second, which is defined as the ( )
the use of high-frequency signals to carry information
asynchronous vs. synchronous communication
Full duplex vs. half duplex
Multiplexing