## Slide 1: 컴퓨터 네트워크 Computer Networks and Internets, 6e

## Slide 2: Chapter 23 Support Protocols and Technologies

## Slide 3: Assignment
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
3
2. An IP datagram has the following partial information.
45000054 00030000 2006…….
a) What is the size of the header and the data?
b) Is the packet fragmented?
c) What is the protocol number of the payload being carried by the packet?
d) How many more routers can the packet travel to?
2. An IP fragment has arrived with a fragment offset value of 100. How many bytes of data were originally sent by the source before the data in this fragment?
3. Capture packets using Wireshark, and explain fields in the IP header.
Send your solution to me by email. (Due date: Sat./ 24PM )
This assignment will be used to check your attendance.
Notes: 3

## Slide 4: IP Datagram

## Slide 5: 23.1 Introduction
This chapter
  continues the discussion of internetworking by introducing four key support technologies:
    address binding
    error reporting
    bootstrapping
    address translation
  Each technology handles a small problem
  When combined with other protocols
    each makes a significant contribution to the overall functionality
Future chapters
  extend the discussion of internetworking
    by focusing on transport layer protocols and Internet routing protocols

## Slide 6
23.7 The Conceptual Address Boundary

## Slide 7: Thought Problem
ARP is sometimes cited as a security weakness
If someone gains access to a given network, how can they exploit ARP to intercept packets?

## Slide 8: 23.8 Internet Control Message Protocol (ICMP)
IP defines a best-effort communication service
  datagrams can be lost, duplicated, delayed, or delivered out of order
It seems best-effort service does not need error detection!
  But IP attempts to avoid errors and to report problems when they occur
We have already seen one example of error detection in IP:
  Header checksum is used to detect transmission errors
  When a host creates an IP datagram
    the host includes a checksum that covers the entire header
  Whenever a datagram is received
    the checksum is verified to ensure that the header arrived intact
The IP header contains a TIME TO LIVE field used to prevent a datagram from circulating forever
  if the forwarding tables in routers incorrectly introduce a circular path

## Slide 9: 23.8 Internet Control Message Protocol (ICMP)
Response to a checksum error is following:
  Datagram must be discarded immediately without more processing
IP’s TTL (hop limit) can detect a routing loop
A reassembly timer can detect lost fragments
Only some types of errors can be reported
IP includes a companion protocol, ICMP
  It is used to report errors back to the original source
IP and ICMP are co-dependent
  IP depends on ICMP to report errors
  and ICMP uses IP to carry error messages
Many ICMP messages have been defined
Figure 23.6 lists key ICMP messages and their purpose

## Slide 10
23.8 Internet Control Message Protocol (ICMP)
TYPE (8) CODE(8) Checksum(16)
DATA1 (32) : ID(16) SEQ. No.(16)
DATA2 (variable size)

## Slide 11: 23.8 Internet Control Message Protocol (ICMP)
As in Figure 23.6, ICMP contains two message types:
  messages used to report errors
  messages used to obtain information
For example
  Time Exceeded and Destination Unreachable are for reporting errors
    when a datagram cannot be delivered successfully
A destination is unreachable if no route exists to the address
A datagram times out if
  either the TTL count in the header expires or
  fragments of the datagram do not arrive before the timer expires
Echo Request and Echo Reply do not correspond to an error
  Instead, they are used by the ping application to test connectivity
  When a host receives an echo request message
    ICMP software on a host or router sends an echo reply that carries the same data as the request

## Slide 12: 23.9 ICMP Message Format and Encapsulation
ICMP uses IP to transport each error message:
  when a router has an ICMP message to send
    it creates an IP datagram and encapsulates the ICMP message in it
  the ICMP message is placed in the payload area of the IP datagram
  the datagram is then forwarded as usual
    with the complete datagram being encapsulated in a frame for transmission
Figure 23.7 (below) illustrates the two levels of encapsulation

## Slide 13: ICMP Message

## Slide 14: ICMP Message

## Slide 15: ICMP Message

## Slide 16: 23.9 ICMP Message Format and Encapsulation
If an ICMP error message causes an error
  no error message is sent
The reason should be clear:
  the designers wanted to avoid the Internet becoming congested carrying error messages about error messages

## Slide 17: 23.9 ICMP Message Format and Encapsulation
If an ICMP error message causes an error
  no error message is sent
The reason should be clear:
  the designers wanted to avoid the Internet becoming congested carrying error messages about error messages

## Slide 18: Protocol Configuration
Many items must be set before protocols can be used
  – IP address of each network interface
  Address mask for each network
  Initial values in the forwarding table
Process is known as protocol configuration
Usually occurs when operating system boots
Two basic approaches
  Manual (Used for IP routers or host that has a permanent IP address)
  Automatic(Used primarily for hosts)
  Automatic configuration requires a computer to be able to use a network before the computer’s protocol parameters have been configured.

## Slide 19: Ways To Solve The Paradox
Use layer 2 protocols to obtain layer 3 parameters, then use layer 3 to obtain higher layers
  Historic approach
  – Relied on Ethernet broadcast
  One computer on a network responded to requests
Use layer 3 to obtain all parameters
  – Current approach
  Relies on IP broadcast (IPv4) or multicast (IPv6)
  Means routers can forward requests to a remote server

## Slide 20: Dynamic Host Configuration Protocol (DHCP)
The standard protocol for automatic configuration
Popular in private enterprises as well as with service providers
Host broadcasts/multicasts a request and receives a reply
Single message exchange allows a host to obtain
  An IP address and address mask to use
  The IP address of a default router
  The address of a DNS server
  A DNS name
  The location of an image to boot (optional)
An ISP using DHCP can choose which IP address to assign to a customer at a given time (Client-Server)

## Slide 21: Dynamic Host Configuration Protocol (DHCP)
Significant features of the protocol (at application layer)
– Recovers from loss or duplication
– Host discovers DHCP server once and caches server
address for future interaction
Derived from BOOTstrap Protocol (BOOTP), but adds
dynamic address assignment

## Slide 22: Dynamic Host Configuration Protocol (DHCP)
DHCP server
– Owns a set of IP addresses
– Chooses an address from the set when a request arrives
– Issues a lease for the address for specified time, T
Client
– Obtains an address and starts a timer for T time units
– Uses the address to communicate
– When the timer expires, requests the server renew the lease
– Either receives a renewal and restarts timer or stops
using the address

## Slide 23: 23.15 Network Address Translation (NAT)
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
23
The Internet has expanded and addresses became scarce
  subnet and classless addressing (CIDR) were introduced to help conserve addresses
Another mechanism was invented that allows multiple computers at a site to share a single, globally valid IP address, known as Network Address Translation (NAT)
Most implementations embed NAT in another device
  such as a Wi-Fi wireless access point or an Internet router
Service is transparent
  No change in protocols on local hosts
  No change in protocols on Internet servers
Notes: 23

## Slide 24: 23.15 Network Address Translation (NAT)
Figure 23.9 (below) illustrates a typical arrangement of a site that uses NAT

## Slide 25: 23.16 NAT Operation and Private Addresses
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
25
NAT solves the problem by using two (2) types of addresses
  The NAT device itself is assigned a single globally-valid IP address
Each computer at the site is assigned IPv6 link-local or IPv4 private
NAT device runs a DHCP server to hand out IP addresses to computers at the site
Notes: 25

## Slide 26: NAT Variants
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
26
Basic NAT
  Only translates IP addresses
  Seldom used in practice
NAPT
  Translates IP address and transport-layer port numbers
  Most widely-used type of NAT
Notes: 26

## Slide 27: 23.16 NAT Operation and Private Addresses
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
27
Figure 23.11 (below) illustrates the translations that occur in each direction
Notes: 27

## Slide 28: 23.16 NAT Operation and Private Addresses
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
28
Most implementations of NAT use a translation table
  to store the information needed to rewrite addresses
Figure 23.12 (below) shows a translation table that corresponds to the address mapping in Figure 23.11
Notes: 28

## Slide 29: 23.17 Transport-Layer NAT (NAPT)
Handles TCP, UDP, and ICMP
Translates TCP/ UDP protocol port numbers as well as IP addresses
Permits multiple computers at a site to contact the same Internet service simultaneously without interference
Examples:
  Two computers at a site download songs from iTunes
  Three computers at a site contact Google simultaneously

## Slide 30: 23.17 Transport-Layer NAT (NAPT)
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
30
Computers at site have private addresses assigned from private address block 192.168 / 16
Two computers at the site each contact TCP port 30000 on computer 128 210.19.20
NAPT chooses a new port number for each and translates
Notes: 30

## Slide 31: 23.18 NAT and Servers
NAT system builds a translation table automatically
  by watching outgoing traffic and establishing a new mapping whenever an application at the site initiates communication
Automatic table construction does not work well for communication initiated from the Internet to the site
  For example, if multiple computers at a site each run a web server
    the NAT device cannot know which computer should receive an incoming web connection

## Slide 32: 23.19 NAT Software and Systems for Use at Home
A NAT software can make a PC act as a NAT device
Also, dedicated NAT hardware systems are available at low cost
  Such systems are usually called wireless routers
  The terminology is slightly misleading because such routers also provide wired connections for host computers

## Slide 33
23.19 NAT Software and Systems for Use at Home

## Slide 34: Chapter 24 The Future IP (IPv6)

## Slide 35: 24.1 Introduction
This chapter
  concentrates on the future of the Internet Protocol
  begins by assessing the strengths and limitations of the current version of IP
  considers a new version of IP that the IETF has developed
  explains features of the new version
  shows how they overcome some of the limitations of the current version

## Slide 36: 24.2 The Success of IP
The current IP (IPv4) has been extremely successful
IP has made it possible for the Internet
  to handle heterogeneous networks
  The Hourglass Model (Appls – IP – Networks)
  IP lies in the middle — changing it means changing all
hosts and routers in the Internet
To accommodate heterogeneous hardware, IP defines
  a network-independent addressing scheme
  datagram format
  encapsulations
  fragmentation strategy
The versatility and scalability of IP are evident
  from the applications that use IP and from the size of the global Internet

## Slide 37: 24.3 The Motivation for Change
When IP was defined, the 32 bits IP address were selected
  doing so allowed the Internet could include over a million networks
The global Internet is growing exponentially
  Its size is doubling in less than a year
Motivation for defining a new version of IP?
  the address space limitation
    larger addresses are necessary to accommodate continued growth
  special facilities are needed for some applications
Consequently, when IP is replaced
  the new version should have more features
    For example, is has been argued that a new version of IP should provide a mechanism for carrying real-time traffic to avoid route changes

## Slide 38: 24.3 The Motivation for Change
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
38
A new version of IP should accommodate more complex addressing and routing capabilities
  In particular, it should be possible to configure IP addressing and routing to handle replicated services
For example, Google maintains many data centers
  When a user enters google.com into a browser, it would be efficient if IP passed datagrams to the nearest Google data center
Many current applications allow a set of users to collaborate
  To make collaboration efficient
    Internet needs a mechanism that allows groups to be created or changed
    It needs a way to send a copy of a packet to each participant in a given group
Notes: 38

## Slide 39: 24.5 A Name and a Version Number
Researchers selected IP The Next Generation
  and early reports referred to the new protocol as IPng
  many competing proposals were made for Ipng
New IP version number that was selected as a surprise
  Because the current IP version number is 4 (IPv4)
    the networking community expected the next official version to be 5
    version 5 was assigned to an experimental protocol known as ST
  The new version of IP received 6 as its official version number (IPv6)

## Slide 40: 24.6 IPv6 Features
IPv6 retains many of the successful features of IPv4 design, such as
  Like IPv4, IPv6 is connectionless
  Like IPv4, the header in a datagram contains a maximum number of hops the datagram can take before being discarded
Features of IPv6 can be grouped into a number of broad categories:
Address Size
  Instead of 32 bits, each IPv6 address contains 128 bits.
  The resulting address space is large enough to accommodate continued growth of the world-wide Internet for many decades
  Suffix can be derived from MAC address
  3 level address hierarchy(Global Prefix – Subnet – Interface(64))

## Slide 41: 24.6 IPv6 Features
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
41
Header Format
  The header is completely different from the IPv4 header
  Almost every field in the header has been changed (some were replaced)
Extension Headers
  IPv6 encodes information into separate headers
    A datagram consists of the base IPv6 header followed by zero or more extension headers, followed by data
Support for Real-Time Traffic
  a mechanism exists that allows a sender and receiver to establish a high-quality path and to associate datagrams with that path
  the mechanism is intended for use with audio and video applications
  the mechanism can also be used to associate datagrams with low-cost paths
Extensible Protocol
  IPv6 allows a sender to add additional information to a datagram
  The extension scheme makes IPv6 more flexible than IPv4
    and means that new features can be added to the design as needed
Notes: 41

## Slide 42: 24.7 IPv6 Datagram Format
An IPv6 datagram contains a series of headers
As Figure 24.2 (below) illustrates
  each datagram begins with a base header
  followed by zero or more extension headers
  followed by the payload
  Fields are not drawn to scale
    some extension headers are larger than the base header
    In many datagrams, the size of the payload is much larger than the size of the header

## Slide 43: Address Binding With IPv6
IPv6 does not use ARP
Instead, IPv6 defines a new address binding mechanism known as IPv6 Neighbor Discovery (IPv6-ND)
IPv6-ND
  – Maintains a neighbor cache
  – Keeps the cache up-to-date at all times
IPv6-ND operation
  Sends a multicast request to find neighbors and populate the cache
  Polls neighbors periodically, even if no datagrams are being sent to the neighbor

## Slide 44: IPv6 Configuration
DHCPv6 has been defined, but...
IPv6 prefers a new procedure known as
IPv6 autoconfiguration
General idea: host can generate an address without using a
server
Motivation: allow two hosts to communicate without further
infrastructure
Obtain a network prefix
– Convention is to use a /64 prefix
– Globally-valid prefix can be obtained from a router
– Local-scope prefix created if no router available
Generate a unique suffix (…..start with MAC address)

## Slide 45
IPv6 Addressing

## Slide 46: 24.13 IPv6 Colon Hexadecimal Notation
IPv6 address occupies 128 bits
  writing such numbers can be unwieldy
Consider a 128-bit number in the dotted decimal notation:
  105.220.136.100.255.255.255.255.0.0.18.128.140.10.255.255
To reduce the number of characters used to write addresses
  colon hexadecimal notation, usually abbreviated colon hex
  69DC : 8864 : FFFF : FFFF : 0 : 1280 : 8C0A : FFFF
An additional optimization known as zero compression further reduces the size
  FF0C:0:0:0:0:0:0:B1  FF0C : : B1
Any IPv6 address that begins with 96-zero bits contains an IPv4 address in the low-order 32-bits

## Slide 47: Assignment
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
47
1. Will an ICMP error message is generated if error is found in
a) a datagram having a multicast address ?
b) a datagram carrying an ICMP error message ?
c) a fragmented datagram that is not the first datagram ?
2. Compare NAT and DHCP. Both can solve the problem of a shortage of addresses in an organization, but by using different strategies.
3. Run wireshark and execute ping command.
Capture various packets using Wireshark, and explain fields in ICMP header.
Send your solution to me by email. (Due date: Sat. /24PM)
This assignment will be used to check your attendance.
Notes: 47