## Slide 1: 컴퓨터 네트워크 Computer Networks and Internets, 6e

## Slide 2: Assignment
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
2
1. Will an ICMP error message is generated if error is found in
a) a datagram having a multicast address ?
b) a datagram carrying an ICMP error message ?
c) a fragmented datagram that is not the first datagram ?
2. Compare NAT and DHCP. Both can solve the problem of a shortage of addresses in an organization, but by using different strategies.
3. Capture various packets using Wireshark, and explain fields in ICMP header.
Run wireshark and execute ping command.
Notes: 2

## Slide 3: ICMP Message

## Slide 4: ICMP Message

## Slide 5: UDP: Datagram Transport Service

## Slide 6: End-To-End Principle
Fundamental concept in the Internet
Network provides best-effort packet transport
Endpoints
  Control communication
  Provide all reliability
Consequence
  Some of the most complex protocols in the Internet protocol suite run in hosts rather than in routers.

## Slide 7: Transport Layer
Layer between applications and IP (layer 4)
Allows multiple applications on a given host to communicate with applications on other hosts
Uses IP to carry messages

## Slide 8: Problems A Transport Protocol Can Handle
Accommodate speed mismatch between sender and receiver
Detect and recover from datagram loss
Eliminate duplicate packets
Guarantee that messages arrive in order
Respond to congestion in the Internet
Prevent delayed packets from being misinterpreted
Verify that data was not corrupted during transit
Ensure that each party has agreed to communicate
Note: a given transport protocol may not handle all problems

## Slide 9: Techniques Transport Protocols Use
Application demultiplexing
  Receiver determine which application should receive the packet
Flow-control mechanisms
  Receiver informs sender of acceptable data rate
  Sender limits rate to prevent overrunning the receiver
Congestion control mechanisms
  Receiver or network informs sender about congestion in the network
  Sender reduces data rate (packet rate) until congestion subsides
Sequence numbers
  Sender places a sequence number in each packet
Positive acknowledgement with retransmission
  Receiver sends acknowledgement , Sender retransmits packet
Sliding window

## Slide 10: Transport Protocols Used In The Internet
Two primary transport protocols used in the Internet
  User Datagram Protocol (UDP)
  Transmission Control Protocol (TCP)
Choice determined by application protocol
  Many applications specify the use of a single transport
  (e.g., email transfer uses TCP)
  Some applications allow the use of either (e.g., DNS queries can be sent via UDP or TCP)

## Slide 11: The User Datagram Protocol
Used
  During startup
  For VoIP and some video applications
Accounts for less than 10% of Internet traffic
Blocked by some ISPs
UDP can be characterized as:
End-to-end
  UDP can distinguish among multiple applications running on a given computer
Connectionless
Message-oriented
  UDP sends and receives individual messages

## Slide 12: The User Datagram Protocol
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
12
Best-effort Delivery
  It offers applications the same best-effort delivery semantics as IP
Arbitrary Interaction
  UDP allows an application
    to send to many other applications
    receive from many other applications
    or communicate with exactly one other application
Operating System Independent
  UDP provides a means of identifying application programs
  It does not depend on identifiers used by the local OS
No congestion or flow control
Notes: 12

## Slide 13: End-To-End Communication
UDP provides communication among applications
Sending UDP
  Accepts outgoing message from application
  Places message in a User Datagram
  Encapsulates User Datagram in an IP datagram and sends
Receiving UDP
  Accepts incoming User Datagram from IP
  Extracts message and delivers to receiving application
Note: message is unchanged by the network

## Slide 14: The Connectionless Paradigm
An application using UDP can
  – Send a message to any receiver (universal)
  Send at any time (asynchronous)
  Stop sending at any time (unterminated)
That is, a sender does not
  Inform the network before sending (i.e., does not establish a communication channel)
  Inform the other endpoint before sending
  Inform the network or other endpoint that no more messages will be sent

## Slide 15: Message-Oriented Interface
UDP offers applications a message-oriented interface
Each time an application requests that UDP send data
  UDP places the data in a single message for transmission
  UDP does not divide a message into multiple packets
  UDP does not combine messages for delivery
Message-oriented interface has several consequences:
  On the positive side
    applications preserve data boundaries
      each message will be exactly the same as was transmitted
  On the negative side
    each UDP message must fit into a single IP datagram

## Slide 16: UDP Message Size
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
16
UDP allows up to 64K octet messages
As a practical limit, the size of a User Datagram is limited by payload area in IP datagram
Maximum IP payload is 64K octets minus size of IP header
Therefore, the maximum UDP payload is 64K octets minus size of IP and UDP headers (usually 64K octets minus 28)
Application can choose any message size up to the maximum UDP payload
Optimal UDP message size is S=M–H (no fragmentation)
  M is the path MTU (i.e., minimum MTU on the path)
  H is th–e size of IP and UDP headers
Notes: 16

## Slide 17: UDP Communication Semantics
UDP uses IP for all delivery
UDP provides best-effort delivery semantics as IP
This means messages can be:
  Lost
  Duplicated
  Delayed
  Delivered out-of-order
  Corrupted
UDP's best-effort delivery semantics have important consequences for applications
  An application must either be immune to the problems or the programmer must take additional steps to detect and correct problems

## Slide 18: UDP Communication Semantics
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
18
As an example of an application that can tolerate packet errors, consider an audio transmission
  If the sender places a small amount of audio in each message
At the opposite extreme, consider an on-line shopping application
  Such applications do not use UDP
    because packet errors can have serious consequences
    (e.g., duplication of a message that carries a catalog order can result in
    two orders, with double charges being made to the buyer's credit card)
Notes: 18

## Slide 19: Modes of Interaction and Broadcast Delivery
UDP allows four styles of interaction:
  1-to-1
  1-to-many
  Many-to-1
  Many-to-many
An application using UDP has a choice
A 1-to-many interaction can be achieved as follows
  An application to repeatedly send a message to multiple recipients, UDP allows an application to transmit the message via IP multicast or broadcast
    For example, local broadcast can be specified by using IP's limited broadcast address, 255.255.255.255

## Slide 20: Endpoint Identification with Protocol Port Numbers
How should UDP identify an application as an endpoint?
  UDP could use the same mechanism that the OS uses
  Because UDP must span heterogeneous computers
    no common mechanism exists
For example
  some OS use process identifiers
  others use job names
  and others use task names
To avoid ambiguity
  UDP defines an abstract set of identifiers called protocol port numbers that are independent of the OS
  UDP must provide a mapping between protocol port numbers and the program identifiers that the OS uses
All computers running UDP recognize the standard protocol port numbers, independent of the OS

## Slide 21: Identifying An Application
Both sending and receiving applications need a port number
Assignment of port numbers depends on the type of application (IANA)
Application that offers a standardized service (server)
  Uses a well-known port number for the service
  Value is less than 1024
  TCP: 21 FTP, 22 SSH, 23 Telnet, 25 SMTP, 80 HTTP, 110 POP3
  UDP: 53 DNS, 67 DHCP, 69 TFTP, 161 SNMP
Registered number (1024 – 49151)
Other applications (client)
  Request a port number from the local operating system
  Value is greater than 49151

## Slide 22: UDP Datagram Format
Each UDP message is called a user datagram and consists of two parts:
  a short header that specifies the sending and receiving application
  a payload that carries the data being sent
Figure 25.1 (below) illustrates the user datagram format.

## Slide 23: UDP Encapsulation
Each UDP datagram is encapsulated in an IP datagram for transmission across the Internet
Figure 25.3 (below) illustrates the encapsulation

## Slide 24
The UDP Checksum and the Pseudo Header

## Slide 25
The UDP Packet

## Slide 26
The UDP Packet

## Slide 27: The UDP Checksum and the Pseudo Header
UDP header contains a 16-bit field named UDP checksum (optional)
  A sender can either choose to compute a checksum or set all bits of the checksum field to zero
When a message arrives at the destination
  UDP software examines the checksum field
  and only verifies the checksum if the value is nonzero
UDP uses a ones-complement checksum
To verify that messages to reach the correct destination without incurring the overhead of additional header fields
  UDP extends the checksum
  Includes extra pseudo header that contains IP addresses

## Slide 28: Assignment
© Pearson Education Inc., Upper Saddle River, NJ. All rights reserved.
28
Explain how we can get reliable transfer through unreliable protocol UDP.
2. The following is a dump of a UDP header; 0045DF0000580000
1) Is the packet directed from a client to a server or vice versa?
2) What is the length of the data?
3) How the sender handled checksum for this packet?
3. Capture various Ethernet frames using Wireshark, and explain fields in the Ethernet, IP, and UDP header.
Send your solution to me by email. (Due date: Sat. /24PM)
This assignment will be used to check your attendance.
Notes: 28